## Slide 1: Midterm Presentation Lecture Computer Vision WS 20/21 Bottle Cap Detection by Localizing Regions of Interest
Janelle Pfeifer
Matr.Nr: 9030898
Notes: Hello My Name is Janelle Pfeifer
Hold a Midterm Presentation
Bottel Cap Detection Project of Computer Vision Lecture

## Slide 2: Structure
Topic
Sub Steps
Data
Approach
Intermediate results
Future Steps
Evaluation
Timetable
Notes: The structure in which I will be Presenting
Introduce the Projekt
Show you my Approach
Talk about future plans

## Slide 3: Introduction - Topic
Find positions of bottle caps in videos
Annotate caps in frames
Seperate caps from distractors
Distinguish states: face-up, face-down, deformed
Notes: Topic of the Project is to
Find bottle caps in a static szene of a video
Bottle Caps get added and removed from the during the video
There is one static szene in which the caps lie stil.
The goal is to annotate the caps in a frame of that scene
Only a part of the Frame is relevant.
Bottle Caps distinguished from distractor objects and
Determine state of the cap itself

## Slide 4: Introduction – sub steps
Find static scene in Video
Choose frame
Find cap-container within the frame
Isolate Regions of Interest inside the container
Determine what kind of content the regions show
  -> cap face up, face down, deformed, distractor
Notes: 1,5 – 2,25 Minuten
Taks can be broken down into sub steps

## Slide 5: Material - Data
Mp4 Videos, 10-20 seconds long, 25 fps
Show empty rectangular container
Bottle caps and distractor objects added
Show static shot of caps and container
Caps possibly get removed
Stil Frames of Videos and JSON Files that annotate Positions of caps
Notes: 7,5 – 10,5 Min
Description of setup and your data
Assumptions and prerequisites
Approaches you already have or are going to apply incl. motivation

## Slide 6: Assumptions
Videos follow the guidelines
Bottle caps face down, white
Bottle caps face up colorful
Face up and face down are circular
Can be distinguished by a neural network

## Slide 7: Approach – Static Scene
Find Static Scene in Video
  Calculate mean square error between frames
  Cut into sequences with a threshold
  Ignore sequence that starts with frame 0
  Choose the best two sequences
  Of those choose the sequence that starts the earliest
mse for video 129
threshhold at 50
Notes: Finding static scene
Static scene differences between frames are small
Videos have up to three static seqzences
One at the start, one after bottlecaps are added
One after they are removed
Quantify differences between frames with mean square error
Cut video into seqzences where difference stays below threshold

## Slide 8: Extract Two Frames per Video
‘emptyframe’ at start of video
‘fullframe’ from choosen static scene

## Slide 9: Approach - ROI
Grayscale subtraction of emptyframe and fullframe
Reduce noise with gaussian blur
Apply threshold to convert image to binary
Grow bottle cap regions
  Close holes in the caps
  Make the regions a little larger
Difference for Video 129
Notes: Subtraction of the images shows regions that have changed. Those regions may contain bottle caps
White regions: regions of interest for bottlecaps

## Slide 10: Approach - Analyze the Regions
Separate connected components
Ignore components that are very small
Define bounding box for each component
Crop out box of original rgb-fullframe
Colored connected components

## Slide 11
Cropped out regions placed over original image

## Slide 12: Approach – Analyze the Regions
Individual cropped regions get evaluated by a Tensorflow model
Annotated regions with tensorflow

## Slide 13: Approach - Tensorflow
Object classification with 2D convolution Layers
Trained with cropped Regions of Interests
Classes: FaceDown, FaceUp, Deformed, Distractor,
Notes: 12 Min

## Slide 14: Intermediate results
Notes: Future stepts & evaluation strategy
Discussion, riscs you might be running into, time table

## Slide 15: Intermediate results
Notes: 3 – 3,75 Minuten
Future stepts & evaluation strategy
Discussion, riscs you might be running into, time table

## Slide 16: Intermediate results
Notes: 3 – 3,75 Minuten
Some caps

## Slide 17: Intermediate results
Notes: 3 – 3,75 Minuten
Future stepts & evaluation strategy
Discussion, riscs you might be running into, time table

## Slide 18: Intermediate results
Notes: 3 – 3,75 Minuten
Objects that are close together are seen as one component, one object,
Some objects are seen as two components

## Slide 19: Intermediate results
Notes: 3 – 3,75 Minuten
Shaking Camera and Fluffy carpet leads to a lot of differences in the image
And outside of container

## Slide 20: Future steps
Finding static scene in videos with a shaking camera
Isolate Container and ignore objects outside
Improve Region of Interest Detection
Improve neural network accuracy
Implement automatic evaluation
Notes: Improving on the steps that are already in place

## Slide 21: Evaluation
Use the Fotos and JSON Files from the Video-Packages for automatic evaluation
Evaluate chosen fullframe via difference to frame in Package
Compare number of regions that contain a bottle-cap to JSON
Compare how the regions are placed

## Slide 22: TimeTable due dates
6.1. Improve ROI Detection and add evaluation
13.1. Isolate container and improve frame detection for busy videos
26.1. Project Report

## Slide 23
Notes: 15
Distinguishing Distractors and Deformed Caps will probably pose a challenge. As will overlapping Objects and hard shadows.
I hope you liked the presentation
Goodbey